## Slide 1
Data Preparation
Download required datasets
Prepare input datasets (Sub-set assets, LCM, Floodplain, Centreline, hydrology rasters, geology, DoD)
Create Initial Confinement
Create a Confinement Project
Load Project with datasets
Create Valley Centreline
Run the GNAT FCT tool
Convert to Network Dataset and extract centerline
Run the Confining Margins tool
Add RID field
Update raw confining state, segment and create valley partitions
Identify bridge confinements then “burn” them into RawConfiningState
Run create split points and segment network tool
Run create Valley Cross sections
Create partitions and then remove any unclip floodplain polygons
Transfer data
Run the transfer margin data to segment tool to pass margin based information over to segment
Compute various metrics
Compute stream power index, identify erroneous catchment areas then correct and update
Compute the confinement and constriction ratios
Run metric tools: Margin erodibility geology and scale, Expansion/Contraction ratio, sinuosity, Assign flood defence to margin, Land use intensity per partition
Run transfer DoD data to segment tool
Create the Margin to Segment Look Up Table
Compute bankside/island area of erosion/deposition
Run compute area of erosion/deposition based upon bank lines
Run compute area of erosion/deposition for island bank lines
Run Transfer bank data to segments
Create Risk Map